VEHICLE SPECIFICATION AMENDMENTS

FOR

KANSAS CTD COUNCIL

COURTESY BID

001-24

The following additions, corrections, changes, and notes to the vehicle specifications were made based on input at (or received before) the Pre-Bid Conference call held on February 26, 2024.  The Request for Quotation #001-24 was posted from the Kansas CTD Council on January 29, 2024.  The courtesy bids must be received by the Kansas CTD Council by mail on March 21, 2024 by 12:00 pm or they may be hand delivered to the bid opening prior to 11:00 am on March 25, 2024.

Specification Changes:

MINI-VAN (MV-24)

- The Spcification for the introduction has been replaced with the following:

Vehicles must be of the latest model year in standard production and, of which, parts are stocked, and warranty service is available at one or more points in Kansas or a border city (defined for this purpose as within 1 hour of the Kansas border). Lack of such parts and service may be cause for rejection of the bid. If the current year is not available, then the next future model year shall be supplied using the PPI adjustments per the federal regulatory standards.

- The Specification for ACCESSORIES has been replaced with the following:

ACCESSORIES:  All safety items and air pollution controls required by statute or regulation in effect at the time the vehicle is produced,  dual sunshades, horn, prismatic type day/night mirror, power point, parking brake with warning light, factory standard electronic AM/FM stereo radio  and clock, undercoating, factory tinted glass in all windows, and all other accessories or optional items which may be shown in the proposal shall be installed in each vehicle. Inclusion of DVD Player & Overhead Rail System is not required or recommended. Three sets of keys shall be provided with the vehicle.  The vehicle shall be equipped with the following gauges or warning lights (if available): voltmeter, oil pressure, temperature and fuel. In addition, a spare tire must be provided to be stored at agency facility.

- The Specification for DELIVERY has been replaced with the following:

DELIVERY:  FIRST VEHICLE - The vehicle shall be delivered F.O.B. to the destination designated by the Kansas Department of Transportation (KDOT) at the time the orders are placed and must be fully equipped in accordance with the specifications and proposal.  The delivery shall be made between the hours of 9:00 a.m. to 12:00 noon or 1:00 p.m. to 4:00 p.m., Monday through Friday, except for holidays.  The first unit of every type requires that prior notice of intent to deliver the vehicle must be given, at least 10 business days in advance, to the proper State employee (Taylor Zortman at taylor.l.zortman@ks.gov, and the purchasing organization during normal business hours. The First Vehicle MUST be ready for inspection no later than February 15, 2025. Failure to follow prescribed delivery procedures may result in at least a 2-week delay in payment from KDOT.  The intent is to have the first vehicle delivered to one of our maintenance facilities and have the KCTDC do the inspection.

- The Specification for Schedule Requirements has been replaced with the following:

Schedule requirement for deliveries:

ALL vehicles ordered by 06/30/2024 MUST be delivered prior to 9/30/2025.

RAMP ACCESSIBLE PASSENGER CONVERSION MINI-VAN (RMV-24)

- The Specification for the introduction has been replaced with the following:

Vehicles must be of the latest model year in standard production and, of which, parts are stocked, and warranty service is available at one or more points in Kansas or a border city (defined for this purpose as within 1 hour of the Kansas border). Lack of such parts and service may be cause for rejection of the bid. If the current year is not available, then the next future model year shall be supplied using the PPI adjustments per the federal regulatory standards.

- The Specification for ACCESSORIES has been replaced with the following:

ACCESSORIES:  All safety items and air pollution controls required by statute or regulation in effect at the time the vehicle is produced,  dual sunshades, horn, prismatic type day/night mirror, power point, parking brake with warning light, factory standard electronic AM/FM stereo radio  and clock, undercoating, factory tinted glass in all windows, and all other accessories or optional items which may be shown in the proposal shall be installed in each vehicle. Inclusion of DVD Player & Overhead Rail System is not required or recommended. Three sets of keys shall be provided with the vehicle.  The vehicle shall be equipped with the following gauges or warning lights (if available): voltmeter, oil pressure, temperature and fuel. In addition, a spare tire must be provided to be stored at agency facility.

- The Specification for DOORS has been replaced with the following:

DOORS:

- Sliding Passenger Doors - The vehicle shall be equipped with power operated single, left and right-side mounted (behind left and right-side front passenger doors) doors.  Doors must maintain OEM fit, finish and seal.  Doors must have a minimum opening of 31.5" and a minimum door clearance height of 56" on the left side with the ramp. The drivers-side will be standard OEM sliding-door.

- Driver/Front Passenger Door - Standard.

- Rear Hatch Door – Due to the height of the vehicle, the hatch on the rear door shall be equipped with a strap that will aid in the closing of the hatch or an OEM power rear-lift gate.

Exceptions: ___________________________________

- The Specification for SEATING has been replaced with the following:

SEATING:  Driver's Seat - Standard OEM adjustment.  Seat shall be high backed with multi-positional fore and aft adjustment, reclining seatback, etc.

- FRONT PASSENGER SEAT - standard quick-release manual-adjustment seat.  Seat shall be high backed with multi-positional fore and aft adjustment, reclining seatback, but will not interfere with ramp when seat is in normal position.

- REAR (3rd ROW) SEAT - Standard two or three (2 or 3) passenger capacity, with fold-down seatback, and folding footrests.  The footrests shall be a type that when installed and not in use, can be stowed away in the base of the seat with the front being flush with the base or folds flat against the seat base. The footrests may be automatic retractable type. Footrest retraction should be gradual, not abrupt that could injure a passenger.

All passenger seats shall be forward facing, standard heavy-duty vinyl (no leatherette), of durable type and materials that can be cleaned easily, fully padded for occupant comfort and retention.  All materials used in seats (including driver seat) shall comply with FMVSS burn resistance requirements.  All seat colors shall match the vehicle color and be aesthetically pleasing.  All seats will comply with FMVSS seat anchorage requirements.

Exceptions: ___________________________________

- The Specification for DELIVERY has been replaced with the following:

DELIVERY:  FIRST VEHICLE - The vehicle shall be delivered F.O.B. to the destination designated by the Kansas Department of Transportation (KDOT) at the time the orders are placed and must be fully equipped in accordance with the specifications and proposal.  The delivery shall be made between the hours of 9:00 a.m. to 12:00 noon or 1:00 p.m. to 4:00 p.m., Monday through Friday, except for holidays.  The first unit of every type requires that prior notice of intent to deliver the vehicle must be given, at least 10 business days in advance, to the proper State employee (Taylor Zortman at taylor.l.zortman@ks.gov, and the purchasing organization during normal business hours. The First Vehicle MUST be ready for inspection no later than February 15, 2025. Failure to follow prescribed delivery procedures may result in at least a 2-week delay in payment from KDOT.  The intent is to have the first vehicle delivered to one of our maintenance facilities and have the KCTDC do the inspection.

- The Specification for Schedule Requirements has been replaced with the following:

Schedule requirement for deliveries:

ALL vehicles ordered by 06/30/2024 MUST be delivered prior to 9/30/2025.

FULL SIZE VAN (FSV-24)

The following changes apply to this type of vehicle:

- The Spcification for the introduction has been replaced with the following:

Vehicles must be of the latest model year in standard production and, of which, parts are stocked, and warranty service is available at one or more points in Kansas or a border city (defined for this purpose as within 1 hour of the Kansas border). Lack of such parts and service may be cause for rejection of the bid. If the current year is not available, then the next future model year shall be supplied using the PPI adjustments per the federal regulatory standards.

- The Specification for TIRES has been replaced with the following:

TIRES:  Seven (7) BSW all-season radials to meet the GVWR of the vehicle.  Spare tire to be mounted on rim and mounted on a tire carrier under the rear of the vehicle.  The weight distribution of the vehicle with maximum load shall not load the tires beyond their rated capacity. Tires shall be the best tires available from the OEM and shall carry the full manufacturer’s warranty.

- The Specification for COLOR has been replaced with the following:

COLOR:   Solid color to be specified at order. Standard colors are red and white.  Paint shall be completed in a clean and professional manner with no blatant evidence of overspray or painting over decals or vehicle emblems. Color chart must be included with bid.  The bid price for the base vehicle will include the standard colors. Order form for other colors will be at an additional cost to the agency.  A bid of white paint only is NOT ACCEPTABLE.

- The Specification for SEATING has been replaced with the following:

SEATING: The driver's seat shall be standard OEM. The upholstery covering color of the driver’s seat shall be complementary to the vehicle’s interior color and the other passenger seats, if available (i.e. blue seat with blue interior and blue passenger seats). The seat shall include shoulder and lap restraining belt with retractor and the longest extra length seat belt extender that has been safety tested for this application. Seats must have been tested to meet FMVSS 210. Seats must be compatible with the Aluminum floor system and capable of being move throughout the cabin of the vehicle without the use of tools.  Front passenger seat shall be OEM cloth bucket seat with color to match driver’s seat. Passenger seats shall be covered with performance fabrics that have a water repellant surface. Color options need to be available for agencies to choose from.

- The Specification for ENGINE has been replaced with the following:

ENGINE:  Shall be minimum of 3.5-liter V6 (gasoline) or a 3.5L PFDi engine, and will include an oil filter, air cleaner, and the heaviest duty cooling system capable of providing sufficient cooling capacity for the operation of all the air conditioning equipment contained in these specifications.

Exceptions: ___________________________________

- The Specification for ENGINE-BLOCK HEATER has been moved to OPTIONAL ITEMS

8. ENGINE-BLOCK HEATER:  A 750-watt (minimum) OEM equipment engine heater shall be provided to assist cold weather starting.  It shall be mounted in a manner that the wiring will not contact hot engine parts.  The exterior plug must have a cover to prevent the entry of water.  The plug-in must be accessible from outside the vehicle.

Exceptions: ___________________________________

- The Specification for WHEELCHAIR LIFT – OPTION 1 has been replaced with the following:

Option 1:  MANUAL RIGHT-SIDE SLIDING PASSENGER ENTRY DOOR: An electro-hydraulic or electro-mechanical powered wheelchair lift shall be mounted on the curbside of the vehicle and be accessible via access doors.

Wheelchair lift door shall be the standard OEM manual sliding side door and must be a “dual access” entry for ambulatory and non-ambulatory passengers to enter and exit the vehicle and must provide a minimum of 30” wide entry for ambulatory passengers when the mounting system is retracted. Lift shall be mounted on the curbside of the vehicle.

- The Specification for DELIVERY has been replaced with the following:

DELIVERY:  FIRST VEHICLE - The vehicle shall be delivered F.O.B. to the destination designated by the Kansas Department of Transportation (KDOT) at the time the orders are placed and must be fully equipped in accordance with the specifications and proposal.  The delivery shall be made between the hours of 9:00 a.m. to 12:00 noon or 1:00 p.m. to 4:00 p.m., Monday through Friday, except for holidays.  The first unit of every type requires that prior notice of intent to deliver the vehicle must be given, at least 10 business days in advance, to the proper State employee (Taylor Zortman at taylor.l.zortman@ks.gov, and the purchasing organization during normal business hours. The First Vehicle MUST be ready for inspection no later than February 15, 2025. Failure to follow prescribed delivery procedures may result in at least a 2-week delay in payment from KDOT.  The intent is to have the first vehicle delivered to one of our maintenance facilities and have the KCTDC do the inspection.

- The Specification for Schedule Requirements has been replaced with the following:

Schedule requirement for deliveries:

ALL vehicles ordered by 06/30/2024 MUST be delivered prior to 9/30/2025.

SMALL TRANSIT COMPOSITE/FIBERGLASS BUS (C20-24)

SMALL TRANSIT METAL BUS (M20-24)

The following changes applies to these 2 types of vehicles:

- The Specification for the introduction has been replaced with the following:

Vehicles must be of the latest model year in standard production and, of which, parts are stocked, and warranty service is available at one or more points in Kansas or a border city (defined for this purpose as within 1 hour of the Kansas border). Lack of such parts and service may be cause for rejection of the bid. If the current year is not available, then the next future model year shall be supplied using the PPI adjustments per the federal regulatory standards.

- The Specification for the WIRING SCHEMATICS has been replaced with the following:

WIRING SCHEMATICS: Detailed schematic for the vehicle as well as the bus body shall be provided to each agency at the time of delivery. If not available at the time of delivery due to a delay from the manufacturer, it MUST be provided at the earliest availability at no charge to the agency. The wiring shall be as follows:

- The Specification for TIRES has been replaced with the following:

TIRES:  Seven (7) BSW all-season radials to meet the GVWR of the vehicle.  Spare tire to be mounted on rim and mounted on a tire carrier under the rear of the vehicle.  The weight distribution of the vehicle with maximum load shall not load the tires beyond their rated capacity. Tires shall be the best tires available from the OEM and shall carry the full manufacturer’s warranty.

- The Specification for BODY has been replaced with the following:

BODY:  The body shall be a (steel cage manufactured out of a minimum of 16-gauge metal integrally mounted to the chassis and conform structurally to FMVSS / composite/fiber glass reinforced plastic (FRP) with a resin hardened honeycombed interior wall (not metal) integrally mounted to the chassis and conform structurally to FMVSS). The outside layer of the body shell shall be (of a metal construction (not fiberglass) / a high gloss gel coat composite/fiberglass (not metal) construction). All doors shall be fitted with tinted safety glass windows to provide maximum visibility to the driver. The initial entry step at the passenger door shall not exceed 12 inches in height from the ground. Less than 12" is preferable.

NOTES: This Spec amendment is for both the C20 and the M20 Specs. The items in parentheses are items specific to either the metal composition or the composite composition. The makeup of the vehicle has not been altered in this spec amendment.

Exceptions: ___________________________________

- The Specification for ENGINE-BLOCK HEATER was moved to OPTIONAL ITEMS:

ENGINE-BLOCK HEATER: A 750-watt (minimum) OEM equipment engine heater shall be provided to assist cold weather starting.  It shall be mounted in a manner that the wiring will not contact hot engine parts.  The exterior plug must have a cover to prevent the entry of water.  The plug-in must be accessible from outside the vehicle.

Exceptions: ___________________________________

- The Specification for CAMERA SYSTEM has been replaced with the following:

CAMERA SYSTEM:  A camera system shall be included. Vendor shall submit description, warranty information and literature information of the product with the bid.

- The Specification for DELIVERY has been replaced with the following:

DELIVERY:  FIRST VEHICLE - The vehicle shall be delivered F.O.B. to the destination designated by the Kansas Department of Transportation (KDOT) at the time the orders are placed and must be fully equipped in accordance with the specifications and proposal.  The delivery shall be made between the hours of 9:00 a.m. to 12:00 noon or 1:00 p.m. to 4:00 p.m., Monday through Friday, except for holidays.  The first unit of every type requires that prior notice of intent to deliver the vehicle must be given, at least 10 business days in advance, to the proper State employee (Taylor Zortman at taylor.l.zortman@ks.gov, and the purchasing organization during normal business hours. The First Vehicle MUST be ready for inspection no later than February 15, 2025. Failure to follow prescribed delivery procedures may result in at least a 2-week delay in payment from KDOT.  The intent is to have the first vehicle delivered to one of our maintenance facilities and have the KCTDC do the inspection.

- The Specification for Schedule Requirements has been replaced with the following:

Schedule requirement for deliveries:

ALL vehicles ordered by 06/30/2024 MUST be delivered prior to 9/30/2025.

- The Specification for  REAR FLASHING LIGHTS has been replaced with the following:

REAR FLASHING LIGHTS: Each bus shall be equipped with 7” 
LED rear lights.  These lights shall be activated with the OEM flasher lights are activated.

Exceptions: ___________________________________

- The Optional Item on the bid form has been altered to the following:

_______ 2.	Entrance Door (Manual)	$______/ea.		$______

(This option may cause delays in delivery)

VEHICLE SPECIFICATION AMENDMENTS

FOR

KANSAS CTD COUNCIL

COURTESY BID

001-24

I have received and read the "Vehicle Specification Amendments" and understand that the changes, additions or corrections included supersede the vehicle specifications posted on January 29, 2024.  I also understand that if my company is awarded the courtesy bid on any of the vehicles, I am responsible for complying with the "Vehicle Specification Amendments" and all other specifications when I supply the vehicles ordered.

COMPANY NAME:

SIGNED BY:

DATE:

(This form along with the initialed “Vehicle Specification Amendments” must be submitted along with the other required forms as a part of your bid proposal.)